## Slide 1: Tise Olayinka
Paxman Interview

## Slide 2: Front-end & Back-end Strategy
Client/User
Intranet
  Each Paxman device will be connected to the local network, to be controlled by the app
Application
  Monitoring of multiple devices on site
  Remote control and scheduling of operations
Company - Paxman
Network Connection
  Connection between app, cloud, company
  Cloud server set up to temporarily store client’s device data, containing:
    No patient data
    Sensor readings
    System settings/configuration
Monitoring
Maintenance
Performance updates OTA
  Device data can be optimised by R&D using machine learning algorithms
  Updated configurations are sent OTA to the desired device

## Slide 3: Solution Design
Current System
Updated System
Cap
Sensors
Microcontroller
Cooling System
I/O Display
DS18B20
4.7K Ω
Touch Screen
Monitoring
Maintenance
OTA Updates
R&D
Sensor Data
Network Connection
Remote Connection
Client App
Intranet
Cloud Server
Cyber Security
Firewall
Paxman
Company
Monitoring
Managing Multiple Devices
Wi-Fi Connection

## Slide 4: Technical Development
Connection Code
Raspberry Pi Connection
The MC can be connected to a local network
Here a shared folder can be created that can hold all required data
Sensor Connection
Multiple sensors can be read from using the one-wire bus
Processing
The data once received by the app or company through the cloud can then be processed
Processing includes conversions into correct formats (the sensor stores the temperature without the d.p.) and use in R&D for monitoring optimisation for patient treatments
Interface Processing
Once configured, the data can then be shown through the interface
Some options have been given to showcase the capabilities available
Standard Continuous Monitoring
Displays the current temperature at configured intervals
Alert Mode
Allows the setting of thresholds that raise alerts when crossed
Cloud Monitoring
Uploads the temperature data to the App – online website for this demonstration
Code

## Slide 5: Schematics and Demo
4.7k Ω
Sensor
DS18B20
Microcontroller
VCC
GND
Data
GPIO4
GND
3V3
Raspberry Pi 3B+
Online
Demo Cam
Console Interface

## Slide 6: Conclusion
Upgrades
Network connectivity
Features
Remote connection and monitoring
Costs
App development
Maintenance
Optimisation algorithms for increased performance
Future
Integration with future devices e.g. Cold gloves and socks for CIPN treatment